NOKIA M1122

Rebuilding Nokia M1122 firmware using HyperTerminal and TFTP Server.

# Setup HyperTerminal

Hardware required;

RJ45 to Serial Adapter	(For PC COM Port)

UTP CAT5 X-Over Cable	(For Serial Adapter and CLi Port)

UTP CAT5 Patch Cable	(For M1122 Ethernet Port to PC Network Interface Card)

Configure HyperTerminal with the following com port settings:

Bits per second:	9600

Data bits:		8

Parity		None

Stop Bits:		1

Flow Control:	None

NOTE: Press the enter key to activate the M1122> or MON> prompt. If you receive the MON> prompt skip to Step 4.

# TFTP Application using TFTPD32

- Extract TFTPD32E.zip file to C:\tftpd32

- TFTPD32 has no setup program.

- Copy startup.cfg and Gx1x2220.r0x files to C:\tftpd32.

- To run TFTPD32 just launch the executable file tftpd32.exe.

IMPORTANT

Ensure M1122 is switched ON.

TFTP Server enabled.

M1122> or MON> Prompt is showing on HyperTerminal Screen.

startup.cfg and Gx1x2220.r0x files are copied to TFTP Server Directory.

## NOKIA M1122 REBUILD

1. M1122>restart

in progress ...local MAC=00:40:43:04:07:fc; Using M512/850 eth conf

2. Type 'm' (fast) followed by 'o' (in 10 sec) to activate Monitor

3. MON>dir				(Lists files currently in RAMBUF Memory)

TFFS v0.01: 30 phy.segments, 128 bl/segment, block size=512 seg sz=65536

?þpCHECK-REPAIR start

CHECK-REPAIR complete

Name                Size   Fno

==============================

.pwd.cfg             121 31055

.pwd.bak             121 31056

startup.cfg          337 31053

image.exe         840422 31054

==============================

used = 852348 b (1668 bl)

garb =  53655 b ( 105 bl)

clean= 990829 b (1939 bl)

4. MON>format				(this wipes everything from RAMBUF)

Starting file system format ...

TFFS v0.01: 30 phy.segments, 128 bl/segment, block size=512 seg sz=65536

? 0TFFS v0.01: 30 phy.segments, 128 bl/segment, block size=512 seg sz=65536

?þpFile system format complete

5. MON>dir				(Confirm that all files have been wiped)

Name                Size   Fno

==============================

==============================

used =      0 b (   0 bl)

garb =      0 b (   0 bl)

clean=1896832 b (3712 bl)

6. MON>ipa 192.168.1.1		(Specify IP Address of M1122)

ip=192.168.1.1

ipserver=0.0.0.0

ipgw=0.0.0.0

serverfile=

7. MON>ips 192.168.1.2		(Specify IP Address of TFTP Server)

ip=192.168.1.1

ipserver=192.168.1.2

ipgw=0.0.0.0

serverfile=

8. MON>file startup.cfg		(List file to copy from TFTP Server)

ip=192.168.1.1

ipserver=192.168.1.2

ipgw=0.0.0.0

serverfile=startup.cfg

9. MON>eget				(Uploads file from TFTP Server to M1122)

tftp loader

ip=192.168.1.1

ipserver=192.168.1.2

ipgw=0.0.0.0

serverfile=startup.cfg

loading file........

file size=337

10. MON>wri startup.cfg		(Writes/Stores file to RAMBUF)

Writing successful

11. MON>file gx1x2220.r08	(List firmware to copy from TFTP Server)

ip=192.168.1.1

ipserver=192.168.1.2

ipgw=0.0.0.0

serverfile=gx1x2220.r08

12. MON>eget			(Uploads file from TFTP Server to M1122)

tftp loader

ip=192.168.1.1

ipserver=192.168.1.2

ipgw=0.0.0.0

serverfile=gx1x2220.r08

loading file......................................................

file size=840422

13. MON>wri gx1x2220.r08	(Writes/Stores file to RAMBUF)

Writing successful

14. MON>ren gx1x2220.r08 image.exe	(Rename GX.. file to Image.exe)

renaming gx1x2220.r08 to image.exe

15. MON>dir				(Confirm that files have been stored in RAMBUF)

Name                Size   Fno

==============================

startup.cfg          337     1

image.exe         840422     2

==============================

used = 850304 b (1664 bl)

garb =  52633 b ( 103 bl)

clean= 993895 b (1945 bl)

16. MON>restart			(Reboot M1122)

in progress ...

local MAC=00:40:43:04:07:fc; Using M512/850 eth conf

Type 'm' (fast) followed by 'o' (in 10 sec) to activate Monitor

normal start

search for temporary files..

TFFS v0.01: 30 phy.segments, 128 bl/segment, block size=512 seg sz=65536

?þÀCHECK-REPAIR start

CHECK-REPAIR complete

no temporary files found

loading executable image from file image.exe:

intermediate-load-addr   0x270000

entry-in-self-extr       0x270104

final-load-addr          0x100

packed-appl-length       808742

unpacked-appl-length     2541508

compression-ratio        69%

run-start-addr           0x2000

Nokia Inc. (C) 1999-2001

Nokia Mrouter

rel-Gx1x2220.R08 built on Jun  7 2001 @ 11:08:37 by krol

17. 	login-id:(leave blank)

password: ******* (Telecom)

# Additional M1122 Commands

M1122>show ip if		(Shows Internal/External IP Address of M1122)

ETH     (up)             net-address     net-mask        mtu  phys-address

192.168.1.1     255.255.255.0   1500 00:40:43:04:07:fc

as ETHERNET

VCC1    (up)          	 net-address     net-mask        mtu  phys-address

210.54.110.105  0.0.0.0         1500 00:40:43:04:07:fc

as PPP

M1122>show dsl		(Shows ADSL Speed Rate)

hardware-type             ALCATEL / DMT

hardware-rev             99111601 / POTS / CP

firmware-rev               3.6.70

activity-status              OPER / FULL

near-end                           far-end

maximum-bitrate              9088 kbits                         896 kbits

actual-bitrate  (Downstream) 8064 kbits 		     (Upstream) 832 kbits

noise-margin                  7.5 dB                            9.0 dB

output-power                 12.0 dBm                          19.5 dBm

attenuation                  28.0 dB                           17.0 dB

corr-fast-fec                   0                                 0

corr-intl-fec                   0                                 5

fail-fast-crc                   0                                 0

fail-intl-crc                   0                                 1

fail-fast-hec                   0                                 0

fail-intl-hec                   0                                 0

flaged-alarms                NONE                              NONE

# M1122 Web Browser Interface

- Start your web browser

- Enter the IP Address of your M1122 in the address bar of your web browser and press enter.

- Type in username/password and click ok to proceed.

- Username: leave blank

- Password: Telecom

- The Nokia M1122 Main Page appears.

# Copying files from M1122 to Local Hard Drive

With TFTP Server enabled, type the following command from HyperTerminal;

M1122>copy startup.cfg tftp:/192.168.1.2/windows/startup.cfg

M1122>

This will copy startup.cfg to c:\windows directory.

You can specify an alternative destination folder on your local drive.

You can upload files from M1122 RAMBUF to your local drive.

# Uploading New Firmware

Upload new firmware to M1122 using TFTP Server

M1122>install tftp:/192.168.1.2/tftpd32e/gx1x2220.r0x

Blocks received

Transfer status SUCCESSFUL

M1122>restart

This will install gx1x2220.r0x file from TFTP Server located in c:\tftpd32e to M1122.

If TFTP Server is located in another directory on local drive then you will need to specify location accordingly.